## Slide 1
Timber Construction in Finland and normative developments
Tomi Toratti
Federation of the Finnish Woodworking Industries

## Slide 2: Content of the presentation
Introduction
Timber industry
Urban construction with Timber
Recent developments in Timber Engineering
Normative Development in Europe – standards
Fire regulations
Challenges and conclusions

## Slide 3: Gross value of production
6,5 Mrd
Labour
26 000
2,5 Mrd
Export value
Raw material use
26 Mm3
Finnish wood working industry in numbers

## Slide 4: Finnish Woodworking Industries 2017 600+ companies with one voice
Federation of the Finnish Woodworking Industries
Stair case producers (8)
Log house industry (17)
Joinery industry (40)
Wood preserving industry (16)
Thermowood association (17)
Association of Finnish woodworking and furniture industries (500)
Stora Enso
Wood Products
Metsä Wood
Versowood
UPM Plywood
UPM Timber
Finnish Forest Industry Federation
WoodInfo
Metsä Fibre

## Slide 5: Product based lobbying Four main areas
Norms and regulation
Education
European cooperation
Research and development
Public procurement
Construction regulation
Research focus
Industry needs
Resources in education
Nordic cooperation
fire
energy efficiency
European cooperation CEI-Bois
Balance of the demand and supply
Program coordination
Content of education
LCA, footprint
Resource efficiency
Environment
Material development
End-use
Continuous collapse
Standardization
Removal of regulations against the use of wood and increase of demand
Strengthening the competitiveness of wood products
Increase of knowledge
European lobby work

## Slide 6
The growth of Finnish forests is over 100 mill. m3 per year FOREST BALANCE IN FINLAND 1960-2011
Chart: mill. m3
| 1960 | 61 | 62 | 63 | 64 | 1965 | 66 | 67 | 68 | 69 | 1970 | 71 | 72 | 73 | 74 | 1975 | 76 | 77 | 78 | 79 | 1980 | 81 | 82 | 83 | 84 | 1985 | 86 | 87 | 88 | 89 | 1990 | 91 | 92 | 93 | 94 | 1995 | 96 | 97 | 98 | 99 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
Annual increment | 57.2 | 57.2 | 57.2 | 57.2 | 57.2 | 57.2 | 57.2 | 57.2 | 57.2 | 57.2 | 57.2 | 57.4 | 57.4 | 57.4 | 57.4 | 57.4 | 57.4 | 58 | 59 | 60 | 61 | 63 | 65 | 67 | 68.4 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 77.7 | 78.5 | 79 | 80 | 81 | 83 | 85 | 87 | 89 | 91 | 93 | 95 | 96.5 | 98 | 99.1 | 101 | 102 | 103.7
Total drain | 60.3 | 63.3 | 58.7 | 57.6 | 58 | 55.9 | 54.3 | 54.4 | 54.1 | 57.5 | 58.7 | 55 | 54.8 | 55 | 52 | 40.7 | 40.7 | 43 | 47.4 | 57.1 | 59.7 | 56.01 | 48.45 | 49.34 | 52.28 | 55.18 | 49.6 | 54.1 | 57.11 | 58.73 | 55.12 | 44.65 | 50.98 | 53.78 | 61.67 | 63.57 | 58.97 | 65.75 | 69.38 | 69.38 | 69.97 | 67.72 | 68.71 | 69.9 | 69.93 | 67.33 | 65.38 | 72.93 | 68.94 | 59.7 | 71.47 | 70.92
Industrial roundwood | 31.5 | 33.5 | 32.3 | 33 | 36.8 | 35.8 | 34.9 | 35.1 | 35.6 | 39.8 | 41.1 | 38.4 | 39.2 | 39.9 | 37.8 | 27.8 | 29.1 | 31.3 | 36.4 | 45 | 48.08 | 44.68 | 41.78 | 39.63 | 41.45 | 43.61 | 38.97 | 42.92 | 45.69 | 47.11 | 43.6 | 34.54 | 40.23 | 42.07 | 49.23 | 51 | 46.92 | 52.99 | 55.13 | 55.29 | 55.9 | 53.25 | 54.16 | 55.03 | 55.05 | 52.57 | 50.82 | 57.74 | 51.69 | 41.4 | 52 | 52.33

## Slide 7: The biggest new potential is where decisions are made professionally and where the buildings are big
Chart: 
| Omakotitalot | Rivitalot | Kerrostalot | Julkiset ja liikerakennukset | Teollisuus ja varasto | Maatalous | Muu talonrakentaminen
Puun osuus runkorakenteissa % | 83 | 65 | 1 | 15 | 18 | 49 | 88
Puun osuus ulkoverhouksissa % | 75 | 44 | 4 | 14 | 10 | 46 | 92
Markkinoiden kokonaisvolyymi (1000 m3) | 4551 | 1701 | 4218 | 10265 | 11759 | 4240 | 3560
Source: Tilastokeskus, Rakentamisen tilastot. VTT
Market share of wood in frames %
Market share of wood in facades %
Total potential (1000m3)
Detached houses
Semi-det. houses
Blocs of flats
Public and comm.
Industry and ware.
Agriculture
Other...

## Slide 8
Over 80 % of the single family homes in Finland are wood based

## Slide 9: Multi-storey Wood construction in Finland
First modern multistorey timber buildings in 1996, max 4 storeys,
from 2011 up to 8 storeys possible
81 multi-storey houses 2100 apartments (2018)
51 multi-storey houses under planning or construction

## Slide 10: The construction of wooden block of flats is growing
Lähde: Tilastokeskus, Forecon
Chart: Share of timber frames %m3
| 2010 | 2011 | 2012 | 2013 | 2014
Puun osuus %-m3 | 1 | 2.5 | 3 | 2.5 | 6
Main reasons for good development
2011 and 2018 new fire regulations relaxed the use of wood
Municipalities have been very actively looking for new options to build houses
New type of industrialised building systems and their potential

## Slide 11
Photos: Stora Enso

## Slide 12: Wood in urban construction is gaining popularity

## Slide 13
Eskolantie, Helsinki

## Slide 14
Kivistö, Vantaa

## Slide 15
Puukuokka, Jyväskylä

## Slide 16: The question today is “How to use wood” in new end-uses and urban surroundings?

## Slide 17
Runko PES Timber element standard

## Slide 18: The new industrial building methods
Volume elements
Post and beam
Hybrid technology
Large elements

## Slide 20: Post and beam
Photos: Metsä Wood

## Slide 22
Case Wood City
Notes: Lets then look at another project in Helsinki city center.

## Slide 23
Three different types of building systems:
  Apartments: large panel LVL
  Hotel: pre-fab CLT room modules
  Office: gluelam beams and columns, CLT slabs and LVL panel walls
Ground floor, staircases and elevator shafts in concrete
LEED Gold as minimum target
Wood City
Office building
12 000 m2
180 hotel rooms,
7 000 m2
98 apartments
8 000 m2
Notes: The project comprises three main blocks to be build with three different type of wooden building systems:
  98 apartments in two blocks to be build with LVL system
  180 rooms hotel to be build with ready-made room modules
  12.000 sqm office building, 170 parking spaces
We are targeting minimum LEED gold ceriticate.

## Slide 24
Expectations of Users
and Tenants
Location remains the key selection criteria
Potential risks (fire, noise, humidity control etc.) must be covered with references and tests
Environmental values increasingly important
Wood can strengthen the brand image

## Slide 25: Customer opinion
Comfort
Overall satisfaction
Temperature
Ventilation
Sound insulation
Present condition
Living costs
Satisfaction rate %
FWR/TTY survey 2011:
6 buildings from 1996 – 2003
Flats 157 (24 % of all)
118 answers (75 %)
    Owners 58%
    Rentals 42%

## Slide 26: Schools, kindergardens and elderly centers have also started to use more and more wood Log building

## Slide 28
Architect Janne Pihlajaniemi, Arkkitehdit M3

## Slide 29
Photos: Kontio
Arkkitehtitoimisto Lukkaroinen Oy

## Slide 30
Kindergarten Haapaavesi 2013
1 200 m2

## Slide 31: Technical challenges in Building with Wood

## Slide 32: Challenges in Building with Wood
Challenge | Description
Lack of professionals in the field | Needs for Wood engineering education
Wood as an engineering material | General know-how on: Proof on service life Material variability and structural reliability Effects of moisture Exploitation of architectural possibilities
Technical issues | Design for durability Vibration of floors Fire regulations Connection design Bracing of structures
Regulations, Standards and CE-marking, Eurocodes | Needs participation in standardization

## Slide 33: Normative development

## Slide 34
Product Standards - material properties - intended use - material quality control - production tolerances
- Material moisture Content - CE-marking leads to acceptance in EU
Design standards - Eurocodes
- design equations - safety factors - model assumptions
- ease of use
Execution standards - follow the design - workmanship (air tightness, acoustic gaps) - assembly tolerances - moisture protection - on site quality control
The Standard chain - setting the quality level

## Slide 35
CE marking of Wood Products
Harmonised standards for wood products
EN 13986 Wood-based panels for use in construction
EN 14250 Prefabricated structural members assembled with punched metal plate fasteners
EN 14374 Laminated veneer lumber
EN 14342 Wood flooring
EN 14080 Glued laminated timber and glued solid timber
EN 14081 Strength graded structural timber
EN 14915 Solid wood panelling and cladding
EN 14545 Connectors
EN 14592 Dowel-type fasteners
EN 14229 Wood poles
EN 15497 Structural finger jointed solid timber
To be finalised
EN 16351 Cross laminated timber EN 14732 Prefabricated, structural wall, floor and roof elements

## Slide 36
Open Industrial standard

## Slide 37: Eurocode 5 Design of timber structures - EN 1995-1-1 Common rules and rules for buildings - EN 1995-1-2 Structural fire design - EN 1995-2 Bridges - National annexes are ready and these are being compared - Eurocodes have been in use for several years

## Slide 38: Eurocode 5 Design of timber structures
New generation of the Eurocodes is under work in CEN/TC250/SC5 by 2022
Simplification of the design work
Bring in new research results
New design rules for: - Cross laminated timber CLT - Reinforcements and holes in beams - Timber concrete composite structures - New approaches to connections, stability and floor vibrations

## Slide 39: Fire regulations in Europe

## Slide 40: Block of flats up to 8 floors
1997
B-s2, d0
D-s2, d0
P2 fire class maximum 8 storeys with REI 60 structures
Sprinkler system is required
K210 (4 floors) or K230 (5-8) fire protected structures
A-class insulation materials
Special requirements for eaves, wooden facades (flame traps), emergency exits, balconies
2011

## Slide 45
Fast, Light and Green
Notes: WOOD CONSTRUCTION
Previous program was successful.
Block of flats
Public buildings due to the indoor air quality
Log Houses
Bridges
Renovation and retrofitting

## Slide 46: 6H2O + 6CO2 → C6H12O6 + 6O2

## Slide 47: Other potential areas to use more wood
Renovation of thje old block of flats
Public buildings
Big structures and halls
Bridges

## Slide 48: Where to get information ?

## Slide 51
About 300 registrants expected

## Slide 52
World Conference on timber engineering
Santiago de Chile, 24 – 27 August 2020
About 800 registrants expected

## Slide 53: Спасибо !